## Slide 1: AI BASED BRAIN CONTROLLED WHEEL CHAIR
SUPERVISOR: DR OMAIR INAM
CO-SUPERVISOR: DR MEHMOOD QURESHI
GROUP MEMBERS: MEHAR DIL [FA18-BCE-031]
HUZAIFA MAQSOOD[FA18-BCE-025]
HIRA SHAHID[FA18-BCE-024]

## Slide 2: Outline:
Problem Statement
Objective
Key Contributions
Overview
Methodology
Results
Summary
Project Timeline
Bibliography

## Slide 3: Problem Statement:
“ There is no cure or proper treatment for Locked-In Syndrome, therefore LIS patients always rely on external assistance. LIS Patients are dependent on nutritional and physical therapies to live a better and healthy life”

## Slide 4: Objective:
“Designing reliable and efficient Artificial Intelligence (AI) based Brain Controlled Wheelchair for Locked-In Syndrome Patients to improve their mobility.”

## Slide 5: Key Contributions:
Jaw Movements Detection
AI based Signal Classification
EEG Headset integration with Arduino UNO
Wheelchair Model

## Slide 6: What is LIS? [1]
Locked-In Syndrome
Serious Neurological Disorder
Causes:
Damage Pons
Tumors
Amyotrophic lateral Sclerosis (ALS)
LIS Patients: [1][4]
Survival expectance up to 5-10 years
Possess Cognitive Abilities
Lack of Voluntary Movement
Eyes ,Jaw Movement , posses few Organ’s Sensation
Damage Pons
Normal Pons
Tracery MRI Results [3]
Neurological Disorder [2]
Tony Nicklinson [4]

## Slide 7: LIS Treatments:
No Cure
or
Treatment
Support
Therapy
Physical
Therapy
Nutritional support
Comfort
Care
Prevention of
Respiratory
Complications

## Slide 8: What is Artificial Intelligence?
Capability of thinking
Acting rationally and humanely
Machine Learning is subset of AI
Uses:
Optimizing the search within data
Logic-chains for if-then reasoning
Pattern-detection
Probabilistic models for predicting future outcomes

## Slide 9: Brain-Controlled Wheelchair for Disabled [5]:
Attention level and Eye blink Encounter for wheelchair movement using EEG Headset.
Working Principle:
Fast Fourier Transform (FFT) analysis
Hardware:
Neurosky MindWave EEG headset
Arduino
WheelChair Model
Limitation:
No AI based algorithm is implemented
Flow Chart Block Diagram of Brain Controlled Wheelchair

## Slide 10: Related Work:
EEG-Based Brain-Controlled Wheelchair with Four Different Stimuli Frequencies(2016): [6]
It used the adaptive-network based fuzzy inference system algorithm to control electronic wheelchair movement.
Mind wave wheelchair system(2021): [7]
They used Electroencephalography (EEG) signal manipulation with the Brain-Computer Interface (BCI) which is an emerging technology designed to convert brainwave to real action.

## Slide 11: Proposed Methodology:
Working Diagram
B
Brainlink Mindwave
EEG Headset
Signal
Processing
Machine
Learning
Software Module
Hardware Module
Wheelchair
Model
Input
Output
Data Acquisition
Module
Mechanical /
Electrical
Module

## Slide 12: Data Acquisition (1/2)
Brainlink Mindwave EEG Headset:
Brainlink Lite EEG Dry Electrode Headband Mind Control Brainwave Feedback
Connect Via: Bluetooth
Baud Rate: 57600
Transmission range: 10m
Data transmission: UART
Three Dry electrodes
Brain’s Electrical
Activity Detection

## Slide 13: Data Acquisition (2/2)
Detection of Jaw Movement
Alpha Waves (8-12Hz)
Beta Waves (13-20Hz)
Gamma Waves (20-200Hz)
Serial Communication between headset
and Bluetooth.
UART Communication Protocol
Data Acquisition Module
Master
Slave
Serial Communication

## Slide 14: Signal Processing
Waveforms: [8]
Alpha Waves: Routine Motor Activities
Beta Waves: Attention Problem Solving
Gamma Waves: Intense Mental Thinking
Butterworth Band Pass Filter: [9]
Bandpass filter the signal between 1-13Hz
Notch Filter: [10]
Band stop filter.
Filter the signal at 13Hz
Signal Processing Module
Filters
Butterworth
Bandpass Filter
Notch Filter
Random Forest
Machine
Learning
Alpha waves
Hardware

## Slide 15: Machine Learning
Artificial Models:
Random Forest Classifier:
Machine Learning Algorithm
Performs Regression tasks
Performs Classification tasks
This model gives predicted output

## Slide 16: Data Sets [11] [12]
Source:
McGill University Faculties of Arts, Science
and Engineering, University of Montreal,
Canada
Marley Xiong , Jenisha Patel and Raffi Hotter.
35 different Healthy Person
Sample Rate = 255Hz
Used Keras API for training
One of the Data Set

## Slide 17: Model Structure
30 inputs.
Outputs = 2
Four functions :
Left, Right, Forward and Rest.
3 Hidden Layers
x1
x2
xn
Input layer
Output Layer
Hidden Layers
ReLU
function
ReLU
function
Sigmoid
function
30 inputs
20
neurons
10
neurons
2
outputs

## Slide 18: Model
Jupyter Notebook
Used Dense Model
Random Forest Classifier
Epochs = 10
Adam Optimizer
Activation Functions:
ReLU
Sigmoid
Training a Model

## Slide 19: Validation
Obtained Accuracy : 84%
Confusion Matrix
Accuracy Result of Dataset

## Slide 20: ML to C-Code Implementation
Libraries used:
Training Model :
NumPy
Sklearn
ML to C-code:
MicroML gen
C-code
Training
Model
Jupyter
Arduino IDE
Arduino
UNO
MicroML
Library
Output
Input
NN
Model

## Slide 21: Hardware Working Diagram

## Slide 22: Project Hardware
Brainlink mindwave EEG Headset:
WheelChair Prototype:

## Slide 23: Hardware Components:
Brainlink mindwave EEG Headset
Arduino UNO
16V Battery
L298 Motor Driver
DC Motor x 2
HC-06 Bluetooth Module x 2

## Slide 24: Results
Brain Controlled Wheelchair prototype based on Artificial Intelligence is designed .
Wheelchair model move around using brain waves based on Jaw movements acquired by EEG headset.
Wheelchair Prototype moves right, left , backward, forward and rest as we clench our jaw right, left, fully clench, loosen clench and then no clench respectively.

## Slide 25: Project Working Video

## Slide 26: Summary
Project works on Jaw movements in form brainwaves.
These brain waves acquired through EEG headset in form of signals.
Signals are processed in Jupyter Notebook to give output in form of alpha waves.
Trained ANN model using different datasets which further performs motor functions.
Trained data is burnt on Arduino to drive wheelchair using C code.
Thus, wheelchair model moves to provide assistance to LIS Patients
An AI(Artificial Intelligence) based Brain Controlled Wheel Chair prototype is our final product.

## Slide 27: Limitations
Interfacing of EEG Headset with PC
Loading ANN Model on Arduino Uno
Corruption of large data in Serial Communication
Selection of EEG Headset
Large noise detection in motion signals
Desired EEG Headset was expensive
An abundance of time was consumed in import of EEG Headset

## Slide 28: Future Work
Implementation using more advanced Artificial Intelligence Models.
More Machine Learning algorithms can be implemented with convergent of Random Forest.
More features can be added like location tracking and heartbeat tracking.
More Accuracy can be achieved.
More sensitivity can be maintained.
This work with more amendments can be introduced in to market.

## Slide 29: Project Timeline

## Slide 30: Bibliography
[1] https://www.ncbi.nlm.nih.gov/pmc/articles/PMC549115/
[2] https://dphhs.mt.gov/schoolhealth/chronichealth/neurologicaldisorders.
[3] A case study of Locked-In-Syndrome: Psychologicaland personal perspectives .[online].Available at: https://www.researchgate.net/publication/50986080_A_case_study_of_Locked-In-Syndrome_Psychological
[4] https://www.theguardian.com/uk/2012/aug/22/tony-nicklinson-right-to-die-case
[5] Mohammad Monirujjaman Khan1,* , Shamsun Nahar Safa1 , Minhazul Hoque Ashik 1 , Mehedi Masud2 and Mohammed A. AlZain"Research and Development of a Brain-Controlled Wheelchair for Paralyzed Patients "vol. 123, no. 12, pp. 50–54, 2015.
[5] Arjon Turnip, Member, IEEE, Demi Soetraprawata, Mardi Turnip, Endra Joelianto, Member, IEEE. Vol.8/No.1 (2016) INTERNETWORKING INDONESIA JOURNAL 65 ISSN: 1942-9703 / © 2016 IIJ EEG-Based Brain-Controlled Wheelchair with Four Different Stimuli Frequencies
[7] International Review on Modelling and Simulations (I.RE.MO.S.), Vol. 14, N. 1 ISSN 1974-9821 February 2021 Copyright © 2021 Praise Worthy Prize S.r.l. - All rights reserved https://doi.org/10.15866/iremos.v14i1.17842 18 Mind-Wave Wheelchair System M0azen Abuzaher, Jamil Al-Azzeh.
[8] https://www.researchgate.net/figure/Brain-Waves-Frequencies_fig1_254256161
[9] https://www.electrical4u.com/butterworth-filter/
[10] https://www.electrical4u.com/band-stop-notch-filter/
[11]NeuroTechX-McGill-2019/offline/data/March 4/11_NoJaw_Rest_Left_Right_5secs
[12] https://github.com/NTX-McGill/NeuroTechX-McGill-2019/

## Slide 31: ANY QUESTIONS?

## Slide 32: THANK YOU.

## Slide 33: More Information (1/2)

## Slide 34: More Information (2/2)